## Slide 1: Implement 128-bit AES algorithm on FPGA board using Verilog hardware coding (only encryption part)
Shashank Soni
(20116090) - O8
Tadiparthi Aditya (20116098) - O8
Sainath Rao P
(20116094) - O8
Yash Raj
(20116110) - O8
Dishant Meena
(20116030) - O6
Team
Play In Slide Show Mode Only

## Slide 2
> Role of Co-Players
> Block Diagram
> Algorithm
> Flow Chart
> Timeline
> Problem Statement
AES
Advanced Encryption Standard - 128 Bit

## Slide 3: Problem Statement
Implement 128-bit AES
(Advanced Encryption Standard) algorithm on FPGA board using Verilog hardware coding
(only encryption part).

## Slide 4: Block Diagram

## Slide 5: Flow Chart

## Slide 6: Terminologies
> Ciphertext : Randomly generated 128-bit text string.
> Key: A 4x4 hexadecimal matrix generated from ciphertext. Each round has its separate round key.
> State matrix: A 4x4 hexadecimal matrix of input plain text.
> Word column: Each column of key is referred to as a word, so a key is of four words namely w[0], w[1], w[2], w[3].
> S-box: Predefined 16x16 matrix having permutations of all hexadecimal characters.
> Round constant matrix (rcon matrix): Predefined 4x10 matrix. Each round has a separate rcon value which is used in XOR operation to generate round keys.
> Mix-column matrix: Constant matrix used in mix column operation for matrix multiplication.

## Slide 7: Algorithm / Steps
> Step 1 :Take 128-bit plain text input, ciphertext as input.
> Step 2 : Represent the input and ciphertext in 4x4 matrix, such that each cell is of 1 byte size.
> Step 3 : Convert the plain text and ciphertext into hexadecimal representation.
Description Of Each Round

## Slide 8: Key Generation
Each round key is generated from previous round key by performing following steps.
Let w = {67, 20, 46, 75}
> Step 1 : Left shift the last column (w) of previous round key by 1 unit. Let us call the modified word as x.
X = {20, 46, 75, 67}
> Step 2 : Substitute each cell of the x with corresponding bytes in S-box, name it as y.
Y = {B7, 5A, 9D,85}
> Step 3 : Take XOR with the round constant (z).
> Step 4. Let the word number be i (w[i]). 0 <= i <= 3;
If i is multiple of 4, then w[i] = w[i-4] ^ z.
Otherwise, w[i] = w[i - 1] ^ w[i - 4].
This round key is used in further steps for encryption.

## Slide 9: Substitute bytes
In the state matrix each cell has 8 bits. (a7 a6 a5 a4….. a0).
> Step 1 : Divide it into two parts i.e.., a7 to a4(let say x) and a3 to a0(let say y). The first four bits (a7-a4) represents the row number whereas the other four bits(a3-a0) represent the column number in S-box.
> Step 2 : Replace each cell of state matrix with the corresponding S-box cell.

## Slide 10: Shifting Rows
> First row is not shifted.
> Second row is shifted one unit.
> Third row is shifted two units.
> Fourth row is shifted three units.
Traverse through the four rows and take the j value for each row in Si,j notation of state matrix. Now take the first j units from the left end and insert at the right after the row ends and the final array results in the following way.
Shift 1
Shift 2
Shift 3
No Change

## Slide 11: Mix-column operation
Perform matrix multiplication between state matrix and a constant matrix.
Eg : b0,1 = 02 x a0,1 + 03 x a1,1 + 01 x a2,1 + 01 x a3,1

## Slide 12: Add Round key
Perform XOR operation of each byte with corresponding bytes in round key
This modified state matrix is then further encrypted in next rounds.

## Slide 13: Initial Round
> Do XOR operation of initial state matrix and cipher key K0.
> XOR corresponding cells of state matrix and K0 matrix.
> The new state matrix will be passed for further rounds(Round 1 - Round 10).

## Slide 14: Intermediate Rounds
Intermediate Rounds (Round 1- Round 9)
> Step a : Repeat step b to step e .
> Step b : Perform subyte operation.
> Step c : Perform shift row operation.
> Step d : Perform Mix column operation.
> Step e : Perform Add Round key operation.

## Slide 15: Final Round
> Step a : Perform Subyte operation.
> Step b : Perform Shift row operation.
> Step c : Perform Add Round key operation.
> Final state matrix is the encrypted message :)
Encrytion
Plaintext
Cipher Text

## Slide 16: RTL Verilog Code
`timescale 1ns / 1ps
module AES_encryption(clock, plain_text, c_key, dataout);
input clock;
input [127:0] plain_text, c_key;
output [127:0] dataout;
wire [127:0] r0_out, r1_out, r2_out, r3_out, r4_out, r5_out, r6_out, r7_out, r8_out, r9_out;
wire [127:0] keyout1, keyout2, keyout3, keyout4, keyout5, keyout6, keyout7, keyout8, keyout9;
assign r0_out = c_key ^ plain_text;
Round R1(.clock(clock), .rc(4'b0001), .stateMatrix(r0_out), .in_key(c_key), .out_key(keyout1), .round_out(r1_out));
Round R2(.clock(clock), .rc(4'b0010), .stateMatrix(r1_out), .in_key(keyout1), .out_key(keyout2), .round_out(r2_out));
Round R3(.clock(clock), .rc(4'b0011), .stateMatrix(r2_out), .in_key(keyout2), .out_key(keyout3), .round_out(r3_out));
Round R4(.clock(clock), .rc(4'b0100), .stateMatrix(r3_out), .in_key(keyout3), .out_key(keyout4), .round_out(r4_out));
Round R5(.clock(clock), .rc(4'b0101), .stateMatrix(r4_out), .in_key(keyout4), .out_key(keyout5), .round_out(r5_out));
Round R6(.clock(clock), .rc(4'b0110), .stateMatrix(r5_out), .in_key(keyout5), .out_key(keyout6), .round_out(r6_out));
Round R7(.clock(clock), .rc(4'b0111), .stateMatrix(r6_out), .in_key(keyout6), .out_key(keyout7), .round_out(r7_out));
Round R8(.clock(clock), .rc(4'b1000), .stateMatrix(r7_out), .in_key(keyout7), .out_key(keyout8), .round_out(r8_out));
Round R9(.clock(clock), .rc(4'b1001), .stateMatrix(r8_out), .in_key(keyout8), .out_key(keyout9), .round_out(r9_out));
finalRound R10(.clock(clock), .rc(4'b1010), .rin(r9_out), .finalKey(keyout9), .final_out(dataout));
endmodule
> AESCIPHER.V

## Slide 17: RTL Verilog Code
`timescale 1ns / 1ps
module Round(clock, rc, stateMatrix, in_key, out_key, round_out);
input clock;
input [3:0] rc;
input [127:0] stateMatrix, in_key;
output [127:0]out_key, round_out;
wire [127:0] MixClm, sb ,shiftedRow;
KeyGeneration k(rc, in_key, out_key);
subbytes sub(stateMatrix, sb);
shiftrow sft(sb, shiftedRow);
mixcolumn mx(shiftedRow, MixClm);
assign round_out = MixClm ^ out_key;
endmodule
> ROUND.V

## Slide 18: RTL Verilog Code
`timescale 1ns / 1ps
module finalRound(clock, rc, rin, finalKey, final_out);
input clock;
input [3:0] rc;
input [127:0] rin, finalKey;
output [127:0] final_out;
wire [127:0] sb, shiftedRow, MixClm, out_key;
KeyGeneration k(rc, finalKey, out_key);
subbytes sub(rin, sb);
shiftrow sft(sb, shiftedRow);
assign final_out= shiftedRow ^ out_key;
endmodule
> FINALROUND.V

## Slide 19: RTL Verilog Code
`timescale 1ns / 1ps
module KeyGeneration(rc, in_key, out_key);
input [3:0] rc;
input [127:0] in_key;
output [127:0] out_key;
wire [31:0] word0, word1, word2, word3, temp;
assign word0 = in_key[127:96];
assign word1 = in_key[95:64];
assign word2 = in_key[63:32];
assign word3 = in_key[31:0];
sbox a1(.inputByte(word3[23:16]), .substitutedByte(temp[31:24]));
sbox a2(.inputByte(word3[15:8]), .substitutedByte(temp[23:16]));
sbox a3(.inputByte(word3[7:0]), .substitutedByte(temp[15:8]));
sbox a4(.inputByte(word3[31:24]), .substitutedByte(temp[7:0]));
assign out_key[127:96] = word0 ^ temp ^ rcon(rc);
assign out_key[95:64] = word0 ^ word1 ^ temp ^ rcon(rc);
assign out_key[63:32] = word0 ^ word1 ^ word2 ^ temp ^ rcon(rc);
assign out_key[31:0] = word0 ^ word1 ^ word2 ^ word3 ^ temp ^ rcon(rc);
> KEYGENERATION.V
function [31:0] rcon;
input [3:0] rc;
case(rc)
4'h1: rcon=32'h01_00_00_00;
4'h2: rcon=32'h02_00_00_00;
4'h3: rcon=32'h04_00_00_00;
4'h4: rcon=32'h08_00_00_00;
4'h5: rcon=32'h10_00_00_00;
4'h6: rcon=32'h20_00_00_00;
4'h7: rcon=32'h40_00_00_00;
4'h8: rcon=32'h80_00_00_00;
4'h9: rcon=32'h1b_00_00_00;
4'ha: rcon=32'h36_00_00_00;
default: rcon=32'h00_00_00_00;
endcase
endfunction
endmodule

## Slide 20: RTL Verilog Code
`timescale 1ns / 1ps
module sbox(inputByte, substitutedByte);
input [7:0] inputByte;
output [7:0] substitutedByte;
reg [7:0] substitutedByte;
always @(inputByte)
case (inputByte)
8'h00: substitutedByte =8'h63;
8'h01: substitutedByte=8'h7c;
8'h02: substitutedByte=8'h77;
8'h03: substitutedByte=8'h7b;
..
..
..
..
..
8'hfa: substitutedByte=8'h2d;
8'hfb: substitutedByte=8'h0f;
8'hfc: substitutedByte=8'hb0;
8'hfd: substitutedByte=8'h54;
8'hfe: substitutedByte=8'hbb;
8'hff: substitutedByte=8'h16;
endcase
endmodule
> SBOX.V

## Slide 21: RTL Verilog Code
`timescale 1ns / 1ps
module mixcolumn(shiftedRow, MixClm);
input [127:0] shiftedRow;
output [127:0] MixClm;
assign MixClm[127:120]= mixcolumn32 (shiftedRow[127:120], shiftedRow[119:112], shiftedRow[111:104], shiftedRow[103:96]);
assign MixClm[119:112]= mixcolumn32 (shiftedRow[119:112], shiftedRow[111:104], shiftedRow[103:96], shiftedRow[127:120]);
assign MixClm[111:104]= mixcolumn32 (shiftedRow[111:104],shiftedRow[103:96],shiftedRow[127:120],shiftedRow[119:112]);
assign MixClm[103:96]= mixcolumn32 (shiftedRow[103:96],shiftedRow[127:120],shiftedRow[119:112],shiftedRow[111:104]);
assign MixClm[95:88]= mixcolumn32 (shiftedRow[95:88], shiftedRow[87:80], shiftedRow[79:72], shiftedRow[71:64]);
assign MixClm[87:80]= mixcolumn32 (shiftedRow[87:80], shiftedRow[79:72], shiftedRow[71:64], shiftedRow[95:88]);
assign MixClm[79:72]= mixcolumn32 (shiftedRow[79:72], shiftedRow[71:64], shiftedRow[95:88], shiftedRow[87:80]);
assign MixClm[71:64]= mixcolumn32 (shiftedRow[71:64], shiftedRow[95:88], shiftedRow[87:80], shiftedRow[79:72]);
assign MixClm[63:56]= mixcolumn32 (shiftedRow[63:56], shiftedRow[55:48], shiftedRow[47:40], shiftedRow[39:32]);
assign MixClm[55:48]= mixcolumn32 (shiftedRow[55:48], shiftedRow[47:40], shiftedRow[39:32], shiftedRow[63:56]);
assign MixClm[47:40]= mixcolumn32 (shiftedRow[47:40], shiftedRow[39:32], shiftedRow[63:56], shiftedRow[55:48]);
assign MixClm[39:32]= mixcolumn32 (shiftedRow[39:32], shiftedRow[63:56], shiftedRow[55:48], shiftedRow[47:40]);
assign MixClm[31:24]= mixcolumn32 (shiftedRow[31:24], shiftedRow[23:16], shiftedRow[15:8], shiftedRow[7:0]);
assign MixClm[23:16]= mixcolumn32 (shiftedRow[23:16], shiftedRow[15:8], shiftedRow[7:0], shiftedRow[31:24]);
assign MixClm[15:8]= mixcolumn32 (shiftedRow[15:8], shiftedRow[7:0], shiftedRow[31:24], shiftedRow[23:16]);
assign MixClm[7:0]= mixcolumn32 (shiftedRow[7:0], shiftedRow[31:24], shiftedRow[23:16], shiftedRow[15:8]);
function [7:0] mixcolumn32;
input [7:0] in1, in2, in3, in4;
begin
mixcolumn32[7] = in1[6] ^ in2[6] ^ in2[7] ^ in3[7] ^ in4[7];
mixcolumn32[6] = in1[5] ^ in2[5] ^ in2[6] ^ in3[6] ^ in4[6];
mixcolumn32[5] = in1[4] ^ in2[4] ^ in2[5] ^ in3[5] ^ in4[5];
mixcolumn32[4] = in1[3] ^ in1[7] ^ in2[3] ^ in2[4] ^ in2[7] ^ in3[4] ^ in4[4];
mixcolumn32[3] = in1[2] ^ in1[7] ^ in2[2] ^ in2[3] ^ in2[7] ^ in3[3] ^ in4[3];
mixcolumn32[2] = in1[1] ^ in2[1] ^ in2[2] ^ in3[2] ^ in4[2];
mixcolumn32[1] = in1[0] ^ in1[7] ^ in2[0] ^ in2[1] ^ in2[7] ^ in3[1] ^ in4[1];
mixcolumn32[0] = in1[7] ^ in2[7] ^ in2[0] ^ in3[0] ^ in4[0];
end
endfunction
endmodule
> MIXCOLUMN.V

## Slide 22: RTL Verilog Code
`timescale 1ns / 1ps
module shiftrow(sb,shiftedRow);
input [127:0] sb;
output [127:0] shiftedRow;
assign shiftedRow[7:0] = sb[39:32];
assign shiftedRow[15:8] = sb[79:72];
assign shiftedRow[23:16] = sb[119:112];
assign shiftedRow[31:24] = sb[31:24];
assign shiftedRow[39:32] = sb[71:64];
assign shiftedRow[47:40] = sb[111:104];
assign shiftedRow[55:48] = sb[23:16];
assign shiftedRow[63:56] = sb[63:56];
assign shiftedRow[71:64] = sb[103:96];
assign shiftedRow[79:72] = sb[15:8];
assign shiftedRow[87:80] = sb[55:48];
assign shiftedRow[95:88] = sb[95:88];
assign shiftedRow[103:96] = sb[7:0];
assign shiftedRow[111:104] = sb[47:40];
assign shiftedRow[119:112] = sb[87:80];
assign shiftedRow[127:120] = sb[127:120];
endmodule
> SHIFTROW.V

## Slide 23: RTL Verilog Code
`timescale 1ns / 1ps
module AES_testbench;
reg clock;
reg [127:0] plain_text, c_key;
wire [127:0] encryptedKey;
AES_encryption u1(.clock(clock), .plain_text(plain_text), .c_key(c_key), .dataout(encryptedKey));
initial
begin
clock = 0;
plain_text = 128'h00112233445566778899aabbccddeeff;
c_key = 128'h000102030405060708090a0b0c0d0e0f;
#50;
plain_text = 128'h54776F204F6E65204E696E652054776F;
c_key = 128'h5468617473206D79204B756E67204675;
#50;
plain_text = 128'h3243f6a8885a308d313198a2e0370734;
c_key = 128'h2b7e151628aed2a6abf7158809cf4f3c;
end
endmodule
> AES_TB.V

## Slide 24: Simulation Result 1

## Slide 25: Simulation Result 2

## Slide 26: Simulation Result 3

## Slide 27: Simulation Result 1-3

## Slide 28: Summary & More About AES
> AES is more effective towards brute force attacks. It has 3.4 * 1038 possible128-bit keys.
> Its variable key size feature makes it more efficient.
> AES encryption can be implemented in both hardware and software.
> AES encryption is also significantly faster, so it is ideal for applications, firmware and hardware that require low latency or high output
> It includes self-encrypting disk drives, database encryption and storage.

## Slide 29: OUR TIMELINE Day 1-2 AES ENCRYPTION
> Getting into the project > Research about the AES Algorithm
> Compile & Organize the data
Day 3-4
> Working on Verilog Code (Build)
Day 8-12
> Preparing the Block diagram and Flowchart
Day 4-7
> Test Bench (Debug) & Simulation
Day 13-15
> Prepare the algorithm and data in organised manner
Notes: > Preparing the algorithm and data in organised manner.

## Slide 30: THE TEAM Sainath Rao P
Shashank Soni
> Research about the AES
> Slides and animation
> Preparing algorithm
> Shift rows & Subbytes code build
> Report preperation
> Research about the AES
> Slides and animation
> Preparing algorithm
> Main module & Test Bench code build
> Report preperation
Tadiparthi Aditya
> Research about the AES
> Preparing algorithm
> Slides preparation
> Mix Column & Key Genern code build
> Report preperation
Dishant Meena
> Research about the AES
> Slides preparation
> Block diagram and Flowchart
> Report preperation
> Round Module code build
Yashraj
> Research about the AES
> Block diagram and Flowchart
> Slides preparation
> Report preperation
> S-box code build